## Slide 1
SKYLO REGIONAL HUB
AWS Architecture Design — us-west-2
Staff Cloud Engineer take-home — network, compute, storage, security, and the end-to-end service-time budget
Data ingress from satellite ground stations · containerized 3GPP core processing · single AZ-resilient hub

## Slide 2
CONTEXT
What this hub does, and what it must survive
Two functions
1
Data ingress
High-volume, real-time connectivity data from multiple satellite ground stations, arriving over AWS Direct Connect.
2
Core network processing
Containerized 3GPP core components managing device sessions, processing data, routing traffic.
Regional hub #1 of many — us-west-2, 3 AZs.
Constraints that matter
Resilient to single-AZ failure
Compute scales with traffic
Least-privilege and zero-trust
SOC 2 already in scope org-wide
Everything provisioned as IaC
Must connect to Direct Connect and to other Skylo AWS Organization accounts
Skylo Regional Hub — AWS Architecture
2

## Slide 3
A1 · NETWORK
VPC, subnet tiers, route tables, NAT, TGW attachment
Skylo Regional Hub — AWS Architecture
3

## Slide 4
A1 · CIDR STRATEGY
Three disjoint address families — collision is structural, not conventional
Hub VPCs
10.0.0.0/9
One /16 per hub, sequential from central IPAM. This hub: 10.100.0.0/16.
Ground segments
10.128.0.0/9
One /16 per hub's ground side. This hub: 10.200.0.0/16. Same /8, other half.
Org / shared accounts
172.16.0.0/12
A different RFC1918 block entirely — not a sub-range of 10.0.0.0/8 at all.
The bug this replaces
An earlier placeholder used 10.96.0.0/11 for org CIDRs — which actually overlaps 10.100.0.0/16, the hub's own VPC. AWS's implicit local-route precedence hides the symptom, but it directly contradicts the “no collisions as we add hubs” claim. Three disjoint address families close it structurally: hub ≠ ground ≠ org, permanently.
Pod secondary CIDR (cluster-local, never crosses the TGW): 100.64.0.0/10 — reused identically by every hub, zero IPAM budget consumed.
Skylo Regional Hub — AWS Architecture
4

## Slide 5
WORKED EXAMPLE
Ground source system → pods → customer access
Skylo Regional Hub — AWS Architecture
5

## Slide 6
END-TO-END SERVICE TIME
Ground network to pod API, and pod to customer
~5–30 ms
Ground station → Direct Connect → TGW
Dominated by physical backhaul distance — Skylo's terrestrial link, not this hub's AWS design.
~3–5 ms
AWS-managed hops inside the hub
TGW attach + in-VPC hops, pod to pod, pod to NLB. The only segment this design actually controls.
~20–100+ ms
NLB → IGW → internet → customer
Dominated by the customer's own network distance and access path — outside this hub's control.
Session/application processing time is counted separately — it's workload-dependent, not a network number. And these are order-of-magnitude engineering estimates from AWS's published component characteristics, not benchmarked figures. Conflating illustrative numbers with measured SLIs is exactly the mistake this design avoids repeating.
Skylo Regional Hub — AWS Architecture
6

## Slide 7
A2 · COMPUTE
EKS, chosen against the workload's own networking needs
Why EKS, not ECS
Core-network pods need low-level networking — custom CNI, multiple NICs, host networking for some components. ECS exposes neither launch type at that layer.
Karpenter (not cluster-autoscaler): provisions against actual pending-pod shape — data-ingress and core-processing nodes want different instance types; a fixed ASG per type is the rigidity Karpenter removes.
Telco-core vendor software ships as Helm charts/Operators with CRDs — not ECS task definitions.
Portability: the same core stack can move to the edge or a second cloud later; ECS task definitions don't.
Cost, stated honestly
A heavier operational surface — control-plane upgrades, add-on management, a real on-call skill requirement ECS mostly hides. Accepted because the networking need is non-negotiable, not because Kubernetes is fashionable.
What would reverse this
If this hub's scope turns out to be only stateless session/control logic — nothing needing host networking or a custom CNI — ECS/Fargate drops the operational overhead substantially.
Reversing question: does this hub run the packet-processing workload, or only session/control logic?
Skylo Regional Hub — AWS Architecture
7

## Slide 8
A3 · STORAGE
One service per job, picked for the access pattern
Short-term session state
High throughput, low latency
ElastiCache (Redis/Valkey), multi-AZ
In-memory reads for session lookups, native TTL for expiry, multi-AZ replication for failover.
Long-term connection-log archival
Durability + auditability
S3, Standard → Intelligent-Tiering/Glacier
Durable and cheap at volume; queryable directly (Athena/Glue) for SOC 2 evidence pulls.
Nuance worth stating out loud
Multi-AZ gives infrastructure-level failover automatically — but a cluster-mode-enabled client still needs to be cluster-aware (MOVED/ASK redirects) to benefit from it. “No app-level handling” is only fully true with cluster-mode-disabled behind a client-side proxy. Confirm which posture the client library actually supports.
Skylo Regional Hub — AWS Architecture
8

## Slide 9
A5 · SECURITY & OBSERVABILITY
Zero-trust by default, not bolted on at the end
IRSA — deliberately withheld
Any wildcard (*) action or resource
iam:PassRole / iam:CreateRole
Rights to modify SGs, route tables, or TGW attachments
Cross-account sts:AssumeRole beyond the 1–2 roles actually needed
sg-nlb-public is the only internet-facing SG. sg-eks-private trusts that SG's ID — never 0.0.0.0/0.
First 3 security services
1
AWS Config
the SOC 2 evidence engine + drift detection
2
GuardDuty
“did something bad happen,” near-zero setup
3
Security Hub
aggregates both into one CIS/FSBP view
Top alerting metrics
Pod crash-loop/OOMKilled · P99 session-processing latency · Scheduling/capacity saturation (watching NAT + ElastiCache limits, not just node count)
Logging & monitoring
Amazon Managed Prometheus + Grafana
Kubernetes-native metrics and dashboards
Fluent Bit → OpenSearch
Container + VPC Flow Logs, SOC 2 audit trail
CloudWatch
AWS-service-level signals only (NAT, TGW, ElastiCache) — not forced to carry everything
Skylo Regional Hub — AWS Architecture
9

## Slide 10
REVISION NOTES
What changed from the earlier draft, and why
CIDR collision
10.96.0.0/11 overlapped the hub's own 10.100.0.0/16.
Three disjoint address families (10.0.0.0/9 / 10.128.0.0/9 / 172.16.0.0/12) — structurally impossible to collide.
TGW segmentation
Ground vs. org traffic separation was asserted in prose, not drawn.
Two explicit route tables on the TGW attachment, shown in the diagram.
Public surface
A diagram showed a workload path straight to the internet, bypassing the NLB.
Exactly one public surface: the NLB. Drawn and stated as a hard rule.
Latency figures
Earlier numbers (“5ms,” “2ms”) were invented, not measured.
Ranges, labeled explicitly as order-of-magnitude estimates — not benchmarks.
Skylo Regional Hub — AWS Architecture
10

## Slide 11
SCOPE, AND WHAT I EXPECT TO DEFEND
Ready for the first 30 minutes
Deliberately out of scope here
Region-loss DR (RTO/RPO target and its cost). Single-AZ resilience is the named constraint and is built into the network/compute design already — that's not DR, it's the baseline. Region failover is a real follow-up question with a verbal answer ready; it's kept out of the written artifact so it stays focused on what's asked.
No internal 3GPP sub-function naming (AMF/SMF/UPF) in the diagrams — kept generic as “data-ingress” and “core-network” pods for a simpler conversation.
Trade-offs I'll defend if pushed
EKS over ECS — reverses if the workload turns out to be session/control-only.
TGW attachment in private subnets, no dedicated tgw-attach tier — reverses on a security review.
ElastiCache failover claim depends on the client library being cluster-aware — needs confirming.
Single Direct Connect circuit, as scoped — production hardening would add a second circuit.
Skylo Regional Hub — AWS Architecture
11

## Slide 12
Structure, naming, and boundaries should survive contact with the follow-up questions.
NETWORK-DESIGN.md · DESIGN.md · vpc.md